| Q. The current in a circuit is the same on both sides of a lamp. True or False? A. True | Q. What is the circuit symbol for a bulb? A. | Q. What is the circuit symbol for a resistor? A. |
| --- | --- | --- |
| Q. What is used to measure the current through a device? A. An ammeter | Q. What is the circuit symbol for an ammeter? A. | Q. What is the circuit symbol for a voltmeter? A. |
| Q. What unit is voltage measured in? A. Volts | Q. When a current flows, what moves through the wires? A. Electrons | Q. Would you connect an ammeter in series or parallel with a bulb in order to measure the current passing through it? A. Series |
| Q. What is the circuit symbol for a switch? A. | Q. What is the difference between a cell and a battery? A. A battery is two or more cells | Q. Must a switch be open or closed for a current to flow? A. Closed |
| Q. What energy change takes place when a current flows through a bulb? A. Electrical -> Light | Q. What energy change takes place in the cells? A. Chemical->electrical | Q. If three bulbs are connected in a series circuit and one bulb breaks what happens to the other bulbs? A. They go out |
| Q. If three bulbs are connected in parallel and one bulb breaks what happens to the other bulbs? A. They stay lit | Q. What is used up as electricity flows through a bulb? A. Energy | Q. Would you connect a voltmeter in series or parallel with a bulb in order to measure the voltage across it? A. Parallel |
| Q. What is used to measure the voltage across a device? A. A voltmeter. | Q. What unit is current measured in? A. Amps | Q. What unit is energy measured in? A. Joules |